Fiducial transformation
Scanned Images
Calibration protocol
Measure fiducial
marks in images
GCPs
(3D Coordinates)
Measure GCP
locations in images
Bundle Block Adjustment
(incl. tie point extraction)
Estimated orientation/
calibration parameters
DEM & orthophoto Workflow
Approximate exterior orientation values
Transformed images
Input/Output
Computation
User Input
Optional